## Slide 1: Stress Corrosion Crack (SCC) Identification using Deep Learning
AI specialist:
Camila Jobim
Juliana Cerqueira
Leonardo Barbosa
Oskar Sjostedt

## Slide 2: AGENDA
BUSINESS PROBLEM
AI SOLUTION
ROI & BUSINESS VALUE
DATA
DEVELOPMENT
DEPLOY
NEXT STEPS

## Slide 3: BUSINESS PROBLEM
During service, corrosive gases present in the production fluids, can penetrate to reach the metallic wires building aggressive environments. All this, associated with the residual stresses of the flexible pipeline manufacturing and service process, triggers one of the most dangerous forms of corrosion Stress Corrosion Cracking (SCC) in which may harm the efficiency, causing the fracture of flexible pipe.
In order to access the level of damage to the wires, several dissection from field samples have done has resulted in a substantial number of macrographs depicting cracks and defects (as result of the corrosive environment) in the armor and pressure wires. However, currently, these images are processed manually, which is a time-consuming process taking many hours and is subject to errors. It is important to point out that all these information of crack area and length are used for the flexible pipe lifetime projection.

## Slide 4: BUSINESS PROBLEM
Tensile
Stress
Metallurgy
Corrosive
Enviroment
SCC

## Slide 5: BUSINESS PROBLEM

## Slide 6: BUSINESS PROBLEM
Manually Process
Up to now:
Over 4000 wires analyzed
Over 1000 macrographs performed
About 5 min/macrograph
Total: approximately 83 hours

## Slide 7: AI SOLUTION
Developing a convolutional neural network (CNN) which is a type of Deep Neural Network that is commonly used in computer vision tasks such as image classification, object detection and segmentation.
To achieve this, the UNet architecture was implemented using Keras to have image segmentation based on several imagens from past projects to train the model from different images of two different metallic wires shapes (and pressure wires).
After doing this, the model will be able to perform semantic segmentation on input images to label each pixel to detect the cracks and extract its measures (crack area and its length).

## Slide 8: Deep Neural Network (Convolutional Neural Network – CNN)
UNet architerature using Keras to train the model
  With Deep learning identification
    About 10s/macrography
    About 3h total (1000 macrographs)

## Slide 9: ROI & BUSINESS VALUE

## Slide 10: Deep Neural Network (Convolutional Neural Network – CNN)
ROI Impact & Estimative
    80.5h could be saved over 1k macrographs taken since 2017;
    LCTMAT takes around 5 min to have the crack localization and its area and length, totalizing 83.3h (1k macrographs).
    ROI = 96,7%
    Furthermore, there are several positive qualitative impacts not measured by the ROI such as standardization, reliability and possibility to increase the database providing more data for the projects.
Business Value
Automating the SCC identification using deep learning can provide several benefits, including:
Saving time of technicians and engineers. This frees up engineers to focus on more complex tasks that require their unique experience and skills;
Possibility to generate even more data with no backlog limit for technicians/engineers (needing only a human oversight, as per recent AI Center of Excellence guideline).
Path to industrialization by removing the subjective criteria, leading to standardization;
Data-driven decision making.

## Slide 11: DATA

## Slide 12: DATA
+1200 IMAGES

## Slide 13: DATA
TRAIN MASK

## Slide 14: DEVELOPMENT

## Slide 15: DEVELOPMENT
1 - Difference between Classification, Localization and Detection

## Slide 16: DEVELOPMENT
2 – Semantic segmentation (categorize each pixel as “crack” or “not crack”)
  Random Forest (Decision Trees)
    Issue: overfitting, memory usage
Train dataset
Test dataset

## Slide 17: DEVELOPMENT
3 – Convolutional Neural Networks (CNN)
  UNet

## Slide 18: DEVELOPMENT
3 – Convolutional Neural Networks (CNN)
  UNet
    Sigmoid activation on output layer
    Output is actually not binary, but a probability
    Image below represents a prediction on a model a few epochs in

## Slide 19: DEVELOPMENT
U-net architecture
Metrics:
Binary IoU, Binary Crossentropy

## Slide 20: DEVELOPMENT
Training metrics monitored via Tensorboard
Loss: Binary Crossentropy
Binary IoU (Jaccard)

## Slide 21: DEVELOPMENT
3 – Convolutional Neural Networks (CNN)
  UNet
    Underrepresented images are not well predicted
    Issue:

## Slide 22: DEPLOY

## Slide 23: NEXT STEPS
    Increase number and variability of imagens to train a new model – Data augmentation
    Histogram equalization of images to remove brightness issues
    Improve method to inform image scale
    Inform length, depth and area of cracks on the app
    Generate edges in red as before – Sobel filter
    Deploy app on a server
    Segment batches of images
    General user experience improvements
    Different network architecture